## Slide 1: ERROR ANALYSIS TASK
DONE BY
KV GAGAN YADAV (192412406)
UNDER THE GUIDANCE OF
DR. MARY REEJA Y

## Slide 2: QUESTION
An interpolation filter is accidentally bypassed. The output spectrum contains multiple images. Explain the debugging procedure

## Slide 3
Solution
An interpolation filter (anti-imaging filter) removes unwanted spectral images produced during upsampling. If it is accidentally bypassed, multiple copies of the original spectrum appear at the output.

## Slide 4: Debugging Procedure
1. Observe the Output Spectrum
Use an FFT or spectrum analyzer.
Check for repeated spectral images at multiples of the sampling frequency.
2. Verify the Upsampling Stage
Ensure the interpolation factor (L) is correctly set.
Confirm that zero insertion is performed properly.

## Slide 5
3. Check the Interpolation Filter
Verify that the low-pass interpolation filter is connected and enabled.
Check that it has not been bypassed due to a hardware or software error.
4. Inspect Filter Parameters
Verify the filter coefficients.
Ensure the cutoff frequency is correctly designed to pass the desired signal and reject image frequencies.

## Slide 6
5. Test with a Known Signal Apply a single-tone sine wave as input. If multiple peaks appear in the output spectrum instead of a single peak, the interpolation filter is bypassed or faulty. 6. Restore the Filter Reconnect or enable the interpolation filter. Observe the output spectrum again. Confirm that the unwanted spectral images disappear and only the desired spectrum remains. | 

## Slide 7: Result
After restoring the interpolation filter, the unwanted spectral images are eliminated, leaving only the desired signal spectrum. This improves signal quality and prevents interference.

## Slide 8: Conclusion
The debugging procedure involves analyzing the output spectrum, verifying the interpolation stage and filter connection, checking filter parameters, testing with a known input signal, and restoring the interpolation filter. This ensures proper operation of multirate DSP systems and reliable performance in applications such as 5G mmWave beamforming.

## Slide 9
Thank you…